| Kinematics | v = v0 + a·t x = x0 + v0·t + ½·a·t2 v2 = v02 + 2a·(x – x0) = (v + v0) / 2 |
| --- | --- |
| Newton’s Law | F = m·a Fgravity = m·g g = 9.80 m/s2 |
| Conservation of Energy | KE1 + U1 + Win/out = KE2 + U2 |
| Energy | Kinetik (linear): KElin = ½ mv2 Potential (gravity): Ug = m g y |
| Work | W = F ( d = F d cos |
| Power (electrical) | P = W/t = E/t P = I V = I2 R = (V)2 / R |
| Coulomb force | F = ke q1q2 / r2 ke = 1/4o |
| Electric field | E = F/q = = -( V E = ke q / r2 for a point charge |
| Electric flux | E = |
| Gauss Law | E = = qinside/o = 4ke ( qinside |
| Potential energy | U = UB - UA = = q V |
| Potential | V = U / q = (= keq/r point charge) |
| Capacitance | C = Q/V [ = o A/d parallel plate C] Ceq = C1 + C2 + C3 + … [parallel combination] 1/Ceq = 1/C1 + 1/C2 + 1/C3 + …[series combination] U = Q2/2C = ½ Q V = ½ C (V)2 [energy stored in C] |
| Charging/discharging of Capacitor | q(t) = Q ( (1 - e-t/RC) I(t) = (V/R) ( e-t/RC q(t) = Q ( e-t/RC I(t) = -(V/R) ( e-t/RC |
| Ohm's Law | R = V/I = ( l/A [ = resistivity = 1/] |
| Resistivity / Resistance |  = me / (n q2 ) [ = scattering time]  = o [1 + (T – To)] [temperature dependence] 1/Req = 1/R1 + 1/R2 + 1/R3 + … [parallel] Req = R1 + R2 + R3 + … [series] |

| Magnetic force | FB = q ( v ( B FB = I ( L ( B [force on straight conductor] dFB = I ( ds ( B [force on conductor segment] FB/L = (oI1I2) / (2a) [force between 2 parallel wires] |
| --- | --- |
| Cyclotron motion | r = (mv) / (qB) [radius]  = (qB) / m [frequency] |
| Magnetic Field by a current Ampere’s Law | dB = o/4 ( (I ds ( ) / r2 [Biot-Savart Law] B = (oI) / 2a) [long straight wire] |
| Magnetic Flux | B = |
| Faraday's Law of Induction | emf = (V =) - N ( (dB / dt) |
| Lenz’ Law | the polarity of the induced emf is such that it wants to act ‘against’ the cause. |
| Inductor | emf = (V =) – L ( dI/dt |
| LR circuit | I = V/R ( (1 - e-t/) ‘switch on’ I = V/R ( e-t/t ‘switch off’  = L/R |
| electron mass proton mass elementary charge Coulomb constant Permittivity of free space Permeability of free space Speed of light | me = 9 ( 10-31 kg mp = 2 ( 10-27 kg e = 1.6 ( 10-19 C [electron: -e ; proton: +e] ke = 9 ( 109 Nm2/C2 o = 9 ( 10-12 C2/Nm2 ke = 1 / (4o) o = 4 ( 10-7 Tm /A c = 3 ( 108 m/s |